## Slide 1
Link Layer - Services and
Addressing
S.V.Jansi Rani
Associate Professor / CSE
Computer Networks

## Slide 2: Agenda
Introduction to Link Layer
Link, nodes, services , point ot point and broadcast links
Link Layer Addressing
Three types of addressing, ARP protocol

## Slide 4
    INTRODUCTION
The Internet is a combination of networks glued together by connecting devices (routers or switches). If a packet is to travel from a host to another host, it needs to pass through these networks.

## Slide 5
Communication at the data-link layer

## Slide 6
Nodes and Links
- Node-to-node
- Data unit from one point in the Internet needs to pass through many networks (LANs and WANs) to reach another point.
- LANs and WANs are connected by routers.
- It is customary to refer to the two end hosts and the routers as nodes and the networks in between as links.

## Slide 7
Nodes and Links

## Slide 8
Services
The data-link layer is located between the physical and the network layers
Encapsulate datagram/packet in a frame and decapsulate the datagram /packet from the frame - Analogy
Framing
Flow Control - Producer -Consumer
Error Control
Congestion Control - sometimes in WAN

## Slide 9
A communication with only three nodes

## Slide 10
Two Categories of Links
Data-link layer controls how the medium is used
Point-to-point link or a broadcast link

## Slide 11
Two Sublayers
Data Link Control (DLC) and media access control (MAC)
Media access control (MAC) -specific to broadcast link

## Slide 12
Dividing the data-link layer into two sublayers

## Slide 13
    LINK-LAYER ADDRESSING
The source and destination IP addresses define the two ends but cannot define which links the packet should pass through.
Link Layer address / MAC Address/ Hardware Address /Physical Address
Encapsulated in a frame and two data-link addresses are added to the frame header
These two addresses are changed every time the frame moves from one link to another.

## Slide 14
Ld,Ls,Ns,Nd

## Slide 15
IP addresses and link-layer addresses in a small internet

## Slide 16: More....?
If the IP address of a router does not appear in any datagram sent from a source to a destination, why do we need to assign IP addresses to routers?
Why do we need more than one IP address in a router, one for each interface?
How are the source and destination IP addresses in a packet determined?
How are the source and destination link-layer addresses determined for each link?

## Slide 17
Three Types of addresses
Some link-layer protocols define three types of addresses:
    Unicast
    Multicast
    Broadcast

## Slide 18
Unicast link-layer addresses in the most common LAN, Ethernet, are 48 bits (six bytes) that are presented as 12 hexadecimal digits separated by colons; for example, the following is a link-layer address of a computer.
LSB of first byte should be 0.
Example
A2:34:45:11:92:F1
9.18

## Slide 19
Multicast link-layer addresses in the most common LAN, Ethernet, are 48 bits (six bytes) that are presented as 12 hexadecimal digits separated by colons. LSB of first byte should be 1.
Example
A3:34:45:11:92:F1
9.19

## Slide 20
Broadcast link-layer addresses in the most common LAN, Ethernet, are 48 bits, all 1s, that are presented as 12 hexadecimal digits separated by colons. The following shows a broadcast address:
Example
9.20

## Slide 21
Address Resolution Protocol (ARP)
Anytime a node has an IP datagram to send to another node in a link, it has the IP address of the receiving node. However, the IP address of the next node is not helpful in moving a frame through a link; we need the link-layer address of the next node. This is the time when the Address Resolution Protocol (ARP) becomes helpful.

## Slide 22
Position of ARP in TCP/IP protocol suite

## Slide 23
ARP operation

## Slide 24
Instead of sending one broadcast frame (ARP request), one unicast frame (ARP response), and another unicast frame (for sending the datagram), system A can encapsulate the datagram and send it to the network. System B receives it and keep it; other systems discard it.
Eg: 20 systems. A to B. 180 frames , 18 frames

## Slide 25
ARP packet

## Slide 26
A host with IP address N1 and MAC address L1 has a packet to send to another host with IP address N2 and physical address L2 (which is unknown to the first host). The two hosts are on the same network.
Example
9.26

## Slide 27
Example 9.4

## Slide 28
The internet for our example

## Slide 29
Flow of packets at Alice site

## Slide 30
Flow of activities at router R1

## Slide 33: Outcome
Student should be able to
Understand about link, nodes, point to point and broadcast links
Services of Data Link Layer
Demonstrate the different addressing of link layer
Explalin how ARP works

## Slide 34: Test Your Understanding
A message transfers from A to B via, R1,R2,R3. During intial configuration when R2 sends ARP request, what is link layer address of R3? ______________
List out the functions of link layer __________, _____,_________

## Slide 35: THANK YOU