## Slide 1
MAC -Random Access
S.V.Jansi Rani
Associate Professor / CSE
Computer Networks

## Slide 2: Agenda
ALOHA
CSMA
CSMA -CD
CSMA - CD

## Slide 4
Taxonomy of Multiple-Access / Medium Access protocols

## Slide 5
RANDOM ACCESS
In random access or contention methods, no station is superior to another station and none is assigned the control over another.
No station permits, or does not permit, another station to send.
Station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
No scheduled time - random transmission
Stations compete with one another - contention

## Slide 6
Frames in a pure ALOHA network

## Slide 7
Procedure for pure ALOHA protocol

## Slide 8: Example
The stations on a wireless ALOHA network are a maximum of 600 km apart. If we assume that signals propagate at 3 × 108 m/s, we find
Tp = (600 × 103 ) / (3 × 108 ) = 2 ms.
Find the value of TB for different values of K.
For K = 1, the range is {0, 1}. The station needs to| generate a random number with a value of 0 or 1. This means that TB is either 0 ms (0 × 2) or 2 ms (1 × 2), based on the outcome of the random variable.

## Slide 9
Vulnerable time for pure ALOHA protocol
Tfr - avg frame tr time

## Slide 10: Example
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the requirement to make this frame collision-free?
Solution
Tfr = 200 bits/200 kbps or 1 ms.
Vulnerable time = 2 × 1 ms = 2 ms.
This means no station should send later than 1 ms before this station starts transmission and no station should start sending during the one 1-ms period that this station is sending.

## Slide 11
The throughput for pure ALOHA is S = G × e −2G .
The maximum throughput
Smax = 0.184 when G= (1/2).
Note
G the average number of frames generated by the system during one frame transmission time

## Slide 12: Example
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second
c. 250 frames per second.
The frame transmission time is 200/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, this is 1 frame per millisecond. Then G=1. In this case S = G× e−2 G or S = 0.135 (13.5 percent). This means that the throughput is 1000 × 0.135 = 135 frames. Only 135 frames out of 1000 will probably survive.

## Slide 13
If the system creates 500 frames per second, this is (1/2) frame per millisecond. The load is (1/2). In this case S = G × e −2G or S = 0.184 (18.4 percent). This means that the throughput is 500 × 0.184 = 92 and that only 92 frames out of 500 will probably survive. Note that this is the maximum throughput case, percentagewise.
If the system creates 250 frames per second, this is 1/4 frame per millisecond. The load is (1/4). In this case S = G × e −2G or S = 0.152 (15.2 percent). This means that the throughput is 250 × 0.152 = 38. Only 38 frames out of 250 will probably survive.

## Slide 14
Frames in a slotted ALOHA network

## Slide 15
Vulnerable time for slotted ALOHA protocol

## Slide 16
The throughput for slotted ALOHA is S = G × e−G .
The maximum throughput Smax = 0.368 when G = 1.
Note

## Slide 17: EXAMPLE
A slotted ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second
c. 250 frames per second.
Solution
The frame transmission time is 200/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, this is 1 frame per millisecond. The load is 1. In this case S = G× e−G or S = 0.368 (36.8 percent). This means that the throughput is 1000 × 0.0368 = 368 frames. Only 386 frames out of 1000 will probably survive.

## Slide 18: EXAMPLE
If the system creates 500 frames per second, this is (1/2) frame per millisecond. The load is (1/2). In this case S = G × e−G or S = 0.303 (30.3 percent). This means that the throughput is 500 × 0.0303 = 151. Only 151 frames out of 500 will probably survive.
If the system creates 250 frames per second, this is (1/4) frame per millisecond. The load is (1/4). In this case S = G × e −G or S = 0.195 (19.5 percent). This means that the throughput is 250 × 0.195 = 49. Only 49 frames out of 250 will probably survive.

## Slide 19
Space/time model of the collision in CSMA
First listen/ sense to medium

## Slide 20
Vulnerable time in CSMA

## Slide 21
Behavior of three persistence methods

## Slide 22
Flow diagram for three persistence methods

## Slide 23
Collision of the first bit in CSMA/CD

## Slide 24
Collision and abortion in CSMA/CD

## Slide 25: Example
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time is 25.6 μs, what is the minimum size of the frame?
Tfr = 2 × Tp = 51.2 μs.
This means, in the worst case, a station needs to transmit for a period of 51.2 μs to detect the collision.
Min frame size = 10 Mbps × 51.2 μs = 512 bits or 64 bytes.

## Slide 26
Flow diagram for the CSMA/CD

## Slide 27
Energy level during transmission, idleness, or collision

## Slide 28
CSMA/CA

## Slide 29
In CSMA/CA, the IFS can also be used to define the priority of a station or a frame.
Note

## Slide 30
In CSMA/CA, if the station finds the channel busy, it does not restart the timer of the contention window;
it stops the timer and restarts it when the channel becomes idle.
Note

## Slide 31
Flow diagram for CSMA/CA

## Slide 32
Collision during handshaking
NAV
Hidden station problem

## Slide 33: CHECK YOUR UNDERSTANDING
Which MAC Protocol is used in wireless networks
How is hidden station problem rectified
What is the vulnerable time for CSMA
How priorities are assigned in CSMA/CA

## Slide 34: Outcome
Student should be able to
The random access protocols such as ALOHA, CSMA, CSMA-CA,CSMA-CD

## Slide 35: THANK YOU