## Slide 1
Multiple Access
- Controlled and Channelization Methods
S.V.Jansi Rani
Associate Professor / CSE
Computer Networks

## Slide 2: Agenda
Medium Access Control
  Controlled Access
    Reservation
    Polling
    Token Passing
  Channelization Protocols
    FDMA
    TDMA
    CDMA

## Slide 4
Taxonomy of Multiple-Access / Medium Access protocols

## Slide 5
12-2 CONTROLLED ACCESS
In controlled access, the stations consult one another to find which station has the right to send. A station cannot send unless it has been authorized by other stations.
Reservation Polling Token Passing

## Slide 6
Reservation access method

## Slide 7
Select and poll functions in polling access method

## Slide 8
Logical ring and physical topology in token-passing access method

## Slide 9
CHANNELIZATION
Channelization is a multiple-access method in which the available bandwidth of a link is shared in time, frequency, or through code, between different stations
FDMA
TDMA
CDMA

## Slide 10
In FDMA, the available bandwidth of the common channel is divided into bands that are separated by guard bands.
Note

## Slide 11: FDMA
Specifies a predetermined frequency band for the entire period of communication – stream data
FDM - physical layer technique that combines the loads from low bandwidth channels and transmits them by using a high-bandwidth channel.
The channels that are combined are low-pass.
The multiplexer modulates the signals, combines them, and creates a band-pass signal.
The bandwidth of each channel is shifted by the mux.
FDMA -access method in the data-link layer.
The data link layer in each station tells its physical layer to make a band-pass signal from the data passed to it.

## Slide 12
Frequency-division multiple access (FDMA)

## Slide 13: TDMA
The stations share the bandwidth of the channel in time.
Each station is allocated a time slot during which it can send data.
Problem - synchronization between the different
stations.
Each station needs to know the beginning of its slot and the location of its slot – difficult - propagation delays - use insert guard times
Synchronization - preamble bits - at the beginning of each slot.

## Slide 14: TDMA
TDM - physical layer technique that combines the data from slower channels and transmits them by using a faster channel.
The process uses a physical multiplexer that interleaves data units from each channel.
TDMA- access method in DL
The data-link layer in each station tells its physical layer to use the allocated time slot.

## Slide 15
Time-division multiple access (TDMA)

## Slide 16
In TDMA, the bandwidth is just one channel that is timeshared between different stations.
Note

## Slide 17
In CDMA, one channel carries all transmissions simultaneously.
Note

## Slide 18: CDMA
CDMA is based on coding theory.
Each station is assigned a code, which is a sequence of numbers called chips
They are called orthogonal sequences and have the certain properties

## Slide 19
Simple idea of communication with code

## Slide 20
Chip sequences

## Slide 21: Properties
1. If we multiply each code by another, we get 0.
2. If we multiply each code by itself, we get 4

## Slide 23
Data representation in CDMA

## Slide 24
Decoding of the composite signal for one in CDMA

## Slide 25
Sharing channel in CDMA

## Slide 26
Station 3 wants to listen to station 2, then decode with station 2 code

## Slide 27
Digital signal created by four stations in CDMA

## Slide 28
General rule and examples of creating Walsh tables

## Slide 29
The number of sequences in a Walsh table needs to be N = 2m.
Note

## Slide 30
Find the chips for a network with
a. Two stations b. Four stations
Example
Solution
We can use the rows of W2 and W4 in Figure 12.29:
a. For a two-station network, we have [+1 +1] and [+1 −1].
b. For a four-station network we have [+1 +1 +1 +1], [+1 −1 +1 −1], [+1 +1 −1 −1], and [+1 −1 −1 +1].

## Slide 31
What is the number of sequences if we have 90 stations in our network?
Example
Solution
The number of sequences needs to be 2m. We need to choose m = 7 and N = 27 or 128. We can then use 90 of the sequences as the chips.

## Slide 32
Prove that a receiving station can get the data sent by a specific sender if it multiplies the entire data on the channel by the sender’s chip code and then divides it by the number of stations.
Example
Solution
Let us prove this for the first station, using our previous four-station example. We can say that the data on the channel D = (d1 ⋅ c1 + d2 ⋅ c2 + d3 ⋅ c3 + d4 ⋅ c4). The receiver which wants to get the data sent by station 1 multiplies these data by c1.

## Slide 33
Example
When we divide the result by N, we get d1 .

## Slide 34: Check Your Understanding
Select is used by ____________ station
When same codes are multiplied, the resulting code will be ____.
CDMA shares channel from ____________ stations.

## Slide 35: Outcome
Student should be able to
Explain the various controlled access MAC protocols such as reservation, polling and token passing
Understand the channelization methods such as FDMA, TDMA and CDMA

## Slide 36: THANK YOU