## Slide 1
IEEE 802.11- Wireless LAN
S.V.Jansi Rani
Associate Professor / CSE
Computer Networks

## Slide 2
    AGENDA
Introduction
Architectural comparison
Characteristics
Access Control
IEEE 802.11
Architecture
  BSS,ESS, Station types
MAC Sublayer
  DCF
  PCF
  Fragmentation
  Frame Format
  Frame types
  Addressing mechanism -exposed station problem

## Slide 3
    AGENDA
  Physical Layer
  Bluetooth
    Architecture
      Piconet
      Scatternet
      Bluetooth devices
    Layers
      Bluetooth layer
      Frame format
      Radio layer

## Slide 5: INTRODUCTION

## Slide 6
    INTRODUCTION
Wireless communication is one of the fastest-growing technologies.
The demand for connecting devices without the use of cables is increasing everywhere.
Wireless LANs can be found on college campuses, in office buildings, and in many public areas.

## Slide 7
    INTRODUCTION - Architectural Comparison
  Medium
  Wired - conn-p2p / mp
  Wireless - air - broadcast
Host
  wired -move with MAC address
  wireless - no phy con
Isolated wired LAN & wireless LAN

## Slide 8
Isolated LANs: wired versus wireless

## Slide 9
Connection of a wired LAN and a wireless LAN to other
networks

## Slide 10
Characteristics
Attenuation - signal disperses in all directions, signal strength decreases
Interference - receive signal from others
Multipath Propagation - more than one signal from same sender at different phases
Error -SNR - high

## Slide 11
Access Control
The CSMA/CD algorithm does not work in wireless LANs for three reasons:
Wireless hosts do not have enough power to send and receive at the same time.
The hidden station problem prevents collision detection
The distance between stations can be great.
Wireless LAN uses CSMA/CA

## Slide 12
Hidden station problem

## Slide 13: iEEE 802.11 wlan

## Slide 14
    IEEE 802.11 PROJECT
IEEE has defined the specifications for a wireless LAN, called IEEE 802.11- wireless Ethernet.
Public uses the term WiFi (short for wireless fidelity) as a synonym for wireless LAN.
WiFi, however, is a wireless LAN that is certified by the WiFi Alliance.

## Slide 15
Architecture
The standard defines two kinds of services:
Basic service set (BSS)
Extended service set (ESS).

## Slide 16
Basic service sets (BSSs)

## Slide 17
Extended service set (ESS)
ESS -stationary / mobile stations

## Slide 18: Station Types
No Transition
BSS Transition Mobility
ESS Transition Mobility

## Slide 19
MAC Sublayer
IEEE 802.11 defines two MAC sublayers:
Distributed coordination function (DCF)
Point coordination function (PCF).

## Slide 20
MAC layers in IEEE 802.11 standard

## Slide 21
CSMA/CA and NAV

## Slide 22: Point Coordination Function (PCF)
It is implemented on top of the DCF and is used mostly for time-sensitive transmission.
PCF has a centralized, contention-free polling access method
The AP performs polling for stations that are capable of being polled.
To give priority to PCF over DCF, another interframe space, PIFS, has been defined. PIFS (PCF IFS) is shorter than DIFS.
To prevent domination of PCF, a repetition interval has been designed to cover both contention-free PCF and contention-based DCF traffic.
Beacon frame - NAV

## Slide 23
Example of repetition interval

## Slide 24
Frame format

## Slide 25
Subfields in FC(Frame Control) field

## Slide 26
Values of subfields in control frames

## Slide 27
Control frames

## Slide 28
Addressing Mechanism
The IEEE 802.11 addressing mechanism specifies four cases, defined by the value of the two flags in the FC field, To DS and From DS.
Each flag can be either 0 or 1, resulting in four different situations.
The interpretation of the four addresses (address 1 to address 4) in the MAC frame depends on the value of these flags

## Slide 29
Addressing mechanisms

## Slide 30
Exposed station problem

## Slide 31
Physical Layer
Six specifications
All implementations, except the infrared, operate in the industrial, scientific, and medical (ISM) band, which defines three unlicensed bands in the three ranges 902–928 MHz, 2.400–4.835 GHz, and 5.725–5.850 GHz.

## Slide 32
Specifications

## Slide 33
Physical layer of IEEE 802.11 FHSS

## Slide 34
Physical layer of IEEE 802.11 DSSS

## Slide 35
Physical layer of IEEE 802.11 infrared

## Slide 36
Physical layer of IEEE 802.11b

## Slide 37: Check Your Understanding
What is the use of repetition intervals in WLAN
Difference between PCF and DCF?

## Slide 38: Outcome
Student should be able to
Explain the various categories of Wireless LAN technology
Demonstrate the various wireless specific problems
Explain the frame format and addressing schemes of WLAN

## Slide 39: THANK YOU