## Slide 1
Bluetooth Technology
S.V.Jansi Rani
Associate Professor / CSE
Computer Networks

## Slide 2
    AGENDA
Bluetooth
    Architecture
    Bluetooth Layers
    Single and Multiple Secondary Communication
    Frame Format
    Radio Layer

## Slide 4: BLUETOOTH

## Slide 5
    BLUETOOTH
Bluetooth is a wireless LAN technology designed to connect devices of different functions when they are at a short distance from each other.
A Bluetooth LAN is an ad hoc network.
The devices, sometimes called gadgets, find each other and make a network called a piconet.
Bluetooth (IEEE 802.15) cannot be large

## Slide 6
Architecture
Bluetooth defines two types of networks: piconet and scatternet.
Piconet - 8 stations
Parked state and active state
Device - 1 Mbps with a 2.4-GHz bandwidth

## Slide 7
Piconet

## Slide 8
Scatternet

## Slide 9
Bluetooth Layers
Bluetooth uses several layers that do not exactly match those of the Internet model

## Slide 10
Bluetooth layers

## Slide 11
L2CAP data packet format

## Slide 12
L2CAP
The L2CAP has specific duties: multiplexing, segmentation and reassembly, quality of service (QoS), and group management.
Multiplexing
Accepts data from UL -frames -delivers
Receiver site - accepts a frame from the baseband layer -extracts the data –delivers to appropriate protocol layer.

## Slide 13
L2CAP
Segmentation and Reassembly
Maximum size of the payload field in the baseband layer is 2774 bits, or 343 bytes.
Size of the packet - 339 bytes (excluding 4 bytes header
Need to send a data packet that can be up to 65,535 bytes
L2CAP divides these large packets into segments
L2CAP segments the packets at the source and reassembles them at the destination.

## Slide 14
L2CAP
QOS
Best effort service
Group Management
Another functionality -allow devices to create a type of logical addressing between themselves.
This is similar to multicasting.
For example, two or three secondary devices can be part of a multicast group to receive data from the primary.

## Slide 15
Single-secondary communication

## Slide 16
Multiple-secondary communication

## Slide 17
Frame format types

## Slide 18: Radio Layer
The radio layer is roughly equivalent to the physical layer of the Internet model.
Bluetooth devices are low-power and have a range of 10 m.
Band
Bluetooth uses a 2.4-GHz ISM band divided into 79 channels of 1 MHz each.
FHSS
Bluetooth hops 1600 times per second, which means that each device changes its modulation frequency 1600 times per second.
A device uses a frequency for only 625 μs (1/1600 s) before it hops to another frequency; the dwell time is 625 μs.

## Slide 19: Radio Layer
Modulation
Bluetooth uses a sophisticated version of FSK, called
GFSK (FSK with Gaussian bandwidth filtering).
GFSK has a carrier frequency. Bit 1 is represented by a frequency deviation above the carrier; bit 0 is represented by a frequency deviation below the carrier.
The frequencies, in megahertz, are defined according to the following formula for each channel.
Fc = 2402 + n MHz , n = 0,1,2 3….,78
For example, the first channel uses carrier frequency 2402 MHz (2.402 GHz)
second channel uses carrier frequency 2403 MHz (2.403 GHz).

## Slide 20: Check Your Understanding
What is the basic unit of bluetooth
Which flow control protocol is used in Bluetooth?

## Slide 21: Outcome
Student should be able to
Explain the Bluetooth technology

## Slide 22: THANK YOU